## Slide 1: Multipath for Outbound Delay Reduction

## Slide 2: Mechanism
Each switch has a default “next-hop” rule and TOS byte marking to fast fwd to proxy node
  One action of the rule: send_to_next_hop
The “next hop” switch (probabilistically determined) sends the first packet to proxy with input port number as part of the IPID field.
Proxy sends packet_In message with IPID field to controller for path set up
Controller setup multiple paths in parallel
Core switch rule is simplified to reduce overhead

## Slide 3
Controller
S1
S3
S5
S2
S4
Switch | Match | Action
............ |  | 
10.1.1.1
10.2.2.2
1.
S1 sends packet_in
Parallel flow_mod to S1,S2,…, S5
Flow table entries in S1,S3,S5 for path P1 complete first
Flow table entries in S2, S4 for Path P2 will time out
2.
Initial Flow Tables
Switch | Match | Action
S1 | 10.2.2.2 | Forward to S3
 | * | Forward to S2
S3 | 10.2.2.2 | Forward to S5
S5 | 10.2.2.2 | Forward to 10.2.2.2
………… |  | 
3.
Path P1
Final Flow Tables

## Slide 4
sw1
sw2
sw3
sw4
sw5
Sw1 receives the packet pkt1, it marks the packet with TOS setting to fast fwd in data plane towards proxy.
Proxy sends the packet_in message with IPID field set with input port info to the controller
3. Controller install rules into sw1, sw3, sw5, sw2, sw4
simultaneously (red has higher priority, green
Has lower priority)
4.So potentially, there are two paths sw1 -> sw3 ->
Sw5 (PATH1) and sw1 -> sw2 -> sw4 (PATH2).
5. If controller receives barrier messages from every switch in PATH1, the controller will send PACKET_OUT message to sw1 then sw1 will send buffered pkt1 out. Subsequent packets will follow PATH1.
6. If controller receives barrier messages from every switch in PATH2, the controller will send PACKET_OUT message to sw2 and then sw2 send pkt1 out, and ask sw1 to discard buffered pkt1. If later on all barrier messages from PATH1 arrives, packets will be switched to PATH1 from PATH2
7. Redundant path is eliminated by “soft-timeout”. In 5., sw2 and sw4 rules are timed out. In 6., if PATH1 does not come back, sw1 (high priority rule), sw3 and sw5 will be timed out; if PATH1 Comes back, sw2, sw4 rules will be timed out.

## Slide 5: Experiments
Try it on the testbed. Does it make sense to simulate a network and show the gains?
First, avoid PACKET_IN, just test the outbound latency reduction
  Compare with and without multipath idea
  Settings: change TCAM occupancy and installation rate; see which settings multipath helps
Second, add PACKET_IN, does this make sense? It should be a fixed delay for both cases in the ideal case.

## Slide 6
Proxy
Rule Offloading
Optimal Rule Update
Unmatched
Packets
Data Plane Hardware
Controller
Flow Engineering
Controller App
Switch Agent
packet_in
Flow_mod

## Slide 7
Middlebox
Rule Offloading
Optimal Rule Update
Multipath Probing
Unmatched
Packets
Data Plane Hardware
Controller
Flow Engineering
Controller App
Switch Agent
packet_in
Flow_mod

## Slide 8
R1
R2
R3
R4
R5
R6
B
B
B
B
A
A
S1
S3
S5
S2
S4
10.2.2.2
(a) Topology
A
B
(b) Rules to install at S1
Switch | Rule (Match & Action)
S1 | R6
 | R5
 | RA
 | RB
S3 | R3
 | R1
S2 | R4
 | R2
………… | 
(c) Partition Result

## Slide 9
Controller
sw1
sw3
sw5
sw2
sw4
Switch | Match | Action
sw1 | * | Forward to sw2
............ |  | 
10.1.1.1
10.2.2.2
1.
S2 sends packet_in for sw1
Parallel flow_mod to sw1,sw2,…, sw5
Flow table entries in sw1,sw3,sw5 for Path1 complete first
flow table entries in sw2, sw4 for Path2 will time out
2.
Initial Flow Tables
Switch | Match | Action
sw1 | 10.2.2.2 | Forward to sw3
 | * | Forward to sw2
sw3 | 10.2.2.2 | Forward to sw5
sw5 | 10.2.2.2 | Forward to 10.2.2.2
………… |  | 
3.
Path1